## Slide 1
ECCDH3DES
Team 3 Members: Nico Bellante, Lucas Dahl, Manish Gupta, Xiong-Yao Zha
Lab Section 3
TA: Yunus Akhtar
4/28/15
1

## Slide 2
What have we designed?
We designed a chip used for secure transmission of data.
Our
Chip
Our
Chip
2

## Slide 3
Why would someone want to use your chip?
Using 163 bits as our key size for ECC, we are able to achieve a greater security than RSA with 1024 bit keys.
Our encryption is implemented using a 48 stage pipelined Triple DES algorithm that allows for 64 bits of data to be encrypted on each clock cycle.
3

## Slide 4
Why is this design appropriate for hardware?
We chose to implement ECC using Galois Fields, a domain perfect for hardware.
  Fixed size bit patterns
  Addition in GF is xors
DES was originally designed for hardware.
4

## Slide 5
System Design on FPGA
5

## Slide 6
Sequence of Operations
Upon reset generate and broadcast our Public key using ECC of our Private key
Then we generate a session key using ECC of our Private key and another party's Public key
Finally we encrypt data using Triple DES encryption with our created session key
6

## Slide 7
Internal Architecture
7

## Slide 8
Design Decisions
We chose to optimize the area of our ECC module.
  Our ECC algorithm is only run once before encrypting data.
We chose to pipeline our DES so we could have encrypted data coming out every clock cycle.
8

## Slide 9
Improvements we've made
We reduced the total area from 300 cm^2 down to 3 cm^2 and then further to our final of 36mm^2
We managed to reduce our critical path of ECC down from 8ns down to just under 4ns.
We changed the design of the controller to allow for more user control.
9

## Slide 10
Critical Paths
          DES ECC
10

## Slide 11
Critical Paths
OVERALL
11

## Slide 12
Area
Total Area in mm^2 = 36.58
Chart: Total Area
| 3DES Combinational | 3DES Non-Combinational | ECC Combinational | ECC Non-Combinational | Controller Combinational | Controller Non-Combinational
 | 15216993 | 4942080 | 7292763 | 8377776 | 219879 | 535392
12

## Slide 13
Power
Total power in mW = 9888.442
Chart: Total Power
| 3DES | ECC | Controller
 | 6840 | 2970 | 78.442
13

## Slide 14
Quartus report
Area on the FPGA
FPGA Clock
14

## Slide 15
Design Specific Success Criteria (DSSC)
Demonstrate by simulation of a Verilog test bench:
  That the public keys of A that are generated are correct.
  That the values of Skx and Sky are both generated correctly.
  That the controller module correctly transitions through its states.
  That given a key, the Triple DES encryption gives the correct output values.
15

## Slide 16
ECC Test Results
The generated Public Keys of A and B match that of the python implementation.
Satisfies DSSC #1
16

## Slide 17
ECC Test Results
The generated Session keys of A and B match each other as well as the python implementation.
Satisfies DSSC #2
17

## Slide 18
Controller Test Results
Coming off reset the controller goes through the states of the initial ECC key generation.
A done signal is asserted when ECC has finished.
Satisfies DSSC #3
18

## Slide 19
Controller Test Results
Given a start signal the Controller goes through the states for the ECC session key generation.
A done signal is asserted when ECC has finished.
Satisfies DSSC #3
19

## Slide 20
Controller Test Results
The Controller goes through two initial wait states.
Then it waits for the start signal to be deasserted.
Lastly it deasserts the done signal and goes to the IDLE state after 48 cycle delay.
Satisfies DSSC #3
20

## Slide 21
Triple DES Test Results
21

## Slide 22
Triple DES Test Results
22

## Slide 23
Triple DES Test Results
The output of our module matches that of the online Triple DES encryption using the same key.
Satisfies DSSC #4
23

## Slide 24
Conclusions
Challenges we faced:
  Implementing the ECC algorithms
  Debugging and optimizing ECC
  FPGA implementation
If we were to do this project again we would research alternate algorithms for ECC.
If we had more time we would have improved our design by using a more versatile bus protocol.
24

## Slide 25: Questions?

## Slide 26
Controller:
Diagrams for Reference

## Slide 27
GF_mod:
Diagrams for Reference

## Slide 28
GF_square
Diagrams for Reference

## Slide 29
GF_mult
Diagrams for Reference

## Slide 30
GF_divide
Diagrams for Reference

## Slide 31
Point Addition
Diagrams for Reference

## Slide 32
Point Double
Diagrams for Reference

## Slide 33
Mxy
Diagrams for Reference

## Slide 34
Point Multiplication
Diagrams for Reference

## Slide 35
Triple DES
Diagrams for Reference

## Slide 36
Key Schedule
Diagrams for Reference

## Slide 37
Generate Round Keys
Diagrams for Reference

## Slide 38
DES
Diagrams for Reference

## Slide 39
DES_Round
Diagrams for Reference

## Slide 40
Feistel
Diagrams for Reference

## Slide 41
Diagrams for Reference
S-Box Substitutions

## Slide 42
Diagrams for Reference
S-Box Substitution